## Slide 1
MOTION & POSITION TRACKING SYSTEM USING MPU6050
  ALDRICH MARIAN A
  BARATH M
  ASISH C
  AKASH SAI
TEAM MEMBERS:

## Slide 2
Motion and position tracking plays an important role in monitoring the orientation and movement of objects in real-time. It is widely used in safety systems, automation, sports analysis, and vehicle stability control. The main objective is to detect unsafe motion patterns early and provide alerts or preventive actions to avoid accidents.
INTRODUCTION

## Slide 3
  Breadboard & Jumper wires
COMPONENTS REQUIRED
  ESP32 microcontroller
  MPU6050 (Accelerometer+Gyroscope)
  OLED Display
  Buzzer for Audible Alerts

## Slide 4
WORKING PRINCIPLE
The accelerometer measures acceleration along the X, Y, and Z axes. It works on the principle of a tiny proof mass inside the sensor: when acceleration occurs, this mass deflects, changing the capacitance, which is converted into acceleration values.
The gyroscope measures angular velocity, or how fast the sensor is rotating around each axis. It uses the Coriolis effect—when the device rotates, vibrating structures inside experience a small force, which is translated into rotational speed.
Together, these values allow the MPU6050 to detect orientation, tilt, motion, and rotation in real time. The sensor communicates this data digitally through the I²C interface, making it easy to integrate with microcontrollers like Arduino or ESP32.

## Slide 5
WORKING PRINCIPLE
The ESP32 is a powerful microcontroller with built-in Wi-Fi and Bluetooth capabilities, widely used in IoT and smart device applications .
It has multiple built-in modules like ADC, DAC, PWM, I²C, SPI, UART, and capacitive touch sensors, allowing it to directly interface with a wide range of sensors and devices.
The working principle revolves around combining computation + wireless communication. It processes input data from sensors, executes programmed instructions, and then can send or receive data over Wi-Fi or Bluetooth without needing an extra module.
It operates on 3.3V logic, and its firmware is programmable using platforms like Arduino IDE, MicroPython, or ESP-IDF.

## Slide 6
FLOWCHART

## Slide 7
CIRCUIT CONNECTION:
  Diagram of ESP32 ↔ MPU6050 ↔ OLED ↔ Buzzer
  Mention pin connections (SDA, SCL, VCC, GND, GPIO pins)
OUTPUT:
  OLED displaying acceleration values
  Buzzer beeping when tilt angle > threshold

## Slide 8
  Rider corners bike → MPU6050 detects lean angle
  If lean angle > safe limit (e.g., 45°), buzzer beeps
  If rider is about to fall (sudden angular acceleration + loss of balance detected), airbag system in rider’s jacket deploys
  Prevents accidents by early warning + injury reduction
APPLICATION IN BIKE CORNERING (EXTENSION IDEA):

## Slide 9
  Accident prevention in sharp turns
  Real-time warning system for riders
  Airbag technology for enhanced safety
  Can be extended to cars, Airbag technology , sports
REAL-WORLD IMPACT:

## Slide 10
CONCLUSION
  MPU6050 with ESP32 can track motion & orientation effectively
  Useful in safety systems (bike, automotive, industrial)
  Future Scope: integrate with IoT, AI-based crash prediction

## Slide 11
EXECUTION:

## Slide 12
THANK YOU